## Slide 1: IoT & Security midterm presentation: “Trusted Execution Environments: Survey and Open Source Alternatives”

## Slide 2: What are Trusted Execution Environments?
Secure area inside a processor
Separate secure region/application from untrusted parts
Minimal Requirements:
  Isolation of applications – no software outside of trusted region may access data inside the trusted region
  Attestation (local or remote) – proof that entity is in specific (valid, not modified) state. Typically measure at start and prevent modification through isolation
Threat Models:
  All other software, even privileged kernel, is considered potential adversary
  Sometimes, Hardware attacks are considered
This requires some sort of Hardware support and depending on requirements also Software – Root of Trust

## Slide 3: Why do we need Trusted Execution Environments?
IoT devices are everywhere
IoT devices often have sensitive data
  Health/financial/personal
TEEs can:
  Ensure that applications execute what we expect (integrity)
  Protect data even in potentially hostile environments (confidentiality)
  Typically, don’t ensure execution of application (availability)

## Slide 4: Structure of my report
Introduction/Motivation
  Introduce Trusted Computing/Execution
  Motivate its use in IoT
  Discuss advantage of OpenSource regarding trust
Technical approaches to TEE
  Hardware based requirements
  Single vs multiple secure regions (e.g.: ARM TrustZone, Intel SGX)
  Threat Models and Scope (e.g. SideChannel attacks like Cache misses)
Open Source approaches
  Next slide
In depth analysis
  Two TEE platforms on same ISA

## Slide 5: Width Coverage
Many implementations and concepts for TEE’s exist
  Intel SGX
  Arm TrustZone
  Sancus (on MSP430)
  Sanctum, Keystone, TIMBER-V (on RISC-V)
  Komodo, OP-TEE (ARM TrustZone based)
  MyTEE (mainly software based, only TrustZone CPU security state needed)
Also some reviews/surveys and attack descriptions on TEEs
  “SgxPectre: Stealing Intel Secrets from SGX Enclaves Via Speculative Execution”, N. Roy et. Al., 2020
  “When Oblivious is Not: Attacks against OPAM”, G. Chen et. Al., 2019

## Slide 6: Depth Coverage
Sanctum
  Builds on foundations of SGX (but doesn’t use SGX)
  Developed for RISC-V processor (open hardware)
    But includes Hardware extensions to support enclave model
  Well documented
  Git Repository seems inactive
Keystone
  Build on multiple previous projects, including SGX and Sanctum
  Developed for RISC-V processor (open hardware)
    Does not include hardware changes, is software only
  Highly customizable TEE
  Requires: Hardware Root of Trust (Secure Key Storage + measured boot + Entropy source) for full security – this is not provided by Keystone
Reason: both focus RISC-V, have been around for a while, well cited

## Slide 7: Not focussed
TIMBER-V
  RISC-V based
  Includes ISA changes
  Only MPU needed for memory protection guarantees
  GitHub last updated 6 years ago
Intel Trusted Domain Extensions (TDX)
  Successor of Intel SGX (which is basis of many other TEE’s)
  Main focus is cloud/datacentre
  Not open source
  Intel Atom processors (low power) are discontinued
    Not relevant for IoT considerations
Google Titan
  M2 Version is RISC-V based
  Very little information available
  Co-processor architecture
  Not open source

## Slide 8: Plan for report writing
General: Take more notes while reading
Create list of abbreviations
Reread Survey/Overview papers (1/1.5 weeks)
  Pay close attention to definition / usage or words
Write introduction / basics / motivation part (1 week)
Read papers about specific TEE/attack (4 weeks)
  After each paper, write summary for that paper/aspect
Finish report (2 weeks)

## Slide 9: My open questions
Should I adjust title to include “IoT”?
  Like: “Trusted Execution Environments for the IoT: Survey and Open Source Alternatives”
How do I make sure I cover all the “relevant” TEE’s?
Problems:
  Some recent work (2023/24)
    Very few citations
    Hard to assess the quality
  Lots of abbreviations, hard to remember